## Slide 1
Final Project
IOTDF
group name: Hakuna Matata
members name: B103011004 林芷伃
B103011050 黃郁珊
B103015006 胡庭翊
The team
Pumbaa
Timon
胡庭翊
Simba
林芷伃
黃郁珊

## Slide 2
SUM
Average
128 bits for a complete input data
(16 clk cycles )
8 input data
128 bits shift left 3 bits
(128 *8 data)
up to 131 bits
SUM / 8 data
128 bits
131 shift right 3 bits
Algorithm - Avg
MIN
MAX
compare the first 8 bits(close to MSB) of two input data(each 128 bits)
Compare every 8 bits starting from the MSB ends of the two data.
When A>B or B>A, a positive edge trigger will be generated at the input port of D Flip-flop.
Maximum and minimum values ​​are selected through MUX and output to another register.
Peak
MINMAX
1 round
2 round
Algorithm - (Peak) Max & Min
Algorithm - Extract & Exclude
Extract:
Exclude:

## Slide 3
Structure - Avg
one data is 128 bits => the maximum bit number of the sum of this 8 data(one round) is 131 bits
132-bits Adder
--> 8*16bits Brent-Kung Adder+4bits Full Adder(MSB)
Brent-Kung Adder is one of a parallel prefix adder(PPA).
PPA are the fastest adders with tree structure based.
this adder exists the minimum area.
Structure of DFF
Structure - Max & Min
count
Cycle
1~16
17~32
33~48
49~64
...
compare
output max or min according to the select
store
the stored value will be compared in next stage
Structure - Max & Min
Cycle
1~16
17~32
33~48
49~64
...
Structure - PeakMax & PeakMin
Structure - Extract & Exclude

## Slide 4
  waste of storage space: 128-bit registers & 136-bit register
  large number of clock cycles:
target: smaller area --> execute time will become larger
Known
&
to-be learn issue

## Slide 5
TO-DO LIST
watch all groups’ video and create final structure
first edition code
run synthesis
final code
optimize circuit
final report
胡庭翊
黃郁珊
林芷伃
Member job assignment
final structure
final structure
final structure
extract/exclude
run synthesis
avg
report v1
(peak) max/min
complete code v1
testbench simulation
testbench simulation
testbench simulation
optimize circuit
final papper
optimize circuit
final papper
optimize circuit
final papper

## Slide 6
Project work schedule
Week 1 (12/11-12/17)
Week 2 (12/18-12/24)
Week 3 (12/25-12/31)
Week 4 (1/1-1/7)
structure v1
final structure
(peak) max/min
avg
run synthesis
presentation
report v1
final papper submit
final papper
extract/exclude
complete code v1
optimize circuit

## Slide 7
Possible issue & expected solution
  If input A = B then the value of “equal” will always be 0 and this causes the signal input to D Flip-flop always be 1  can’t generate any positive edge signal to trigger D Flip-flop to output value D
solution: use a counter with a smaller period of clock cycle (compare to input clk signal) to initialize the value to 0 which needed to input to D Flip-flop
0->1
0
0 or 1
0
1->0
1
0 or 1
1 or 0
count
Possible issue & expected solution
2. the output is not what we expected
 write each function in sub-module and compile each of them to debug
THANK
YOU!