## Slide 1: ELECTRICAL ENGINEERING iii FPGA dEVELOPMENT PLATFORM
Quartus (Quartus Prime 20.1) Lite Edition
Ver. 2023/8/28

## Slide 2
1. Download Quartus and add new project
2. Verilog coding, compile, simulate
3. Set device pin, download code to FPGA

## Slide 3: DOWNLOAD
FPGAs website (intel.com) download quartus 20.1 lite edition
Teaching website have Google Drive download link
※Need intel account

## Slide 4: Setup
Download and extract file，open「setup.bat」file.
Accept the agreement.
Choose the installation directory
The installation path cannot contain
Chinese characters.

## Slide 5: setup
Select the componets like picture.

## Slide 6: Create new project
Every implementation need create a new folder belong to the project
Create project
OR

## Slide 7: CREATE NEW PROJECT
Project derectory
Project name
Top-module name, as same as project name

## Slide 8: CREATE NEW PROJECT
Choose empty

## Slide 9
Load in files
Method 1:Before create Method 2:After create
Add all files
Browse files

## Slide 10: CREATE PROJECT
FPGA setting
Family: Cyclone V
Device: Cyclone V SE Mainstream
”Available devices”
Choose:”5CSEMA5F31C6”
5CSEMA5F31C6

## Slide 11: coding
New Verilog HDL File, save module after coding.
The file name should match the module project name. Otherwise, compilation will result in an error.
Verilog code
Add all files

## Slide 12: coding
Set the module as top-level module.
Press compile. If there are no error message, the compile is successful. Having warning message is normal.
Right click
compile
No errors
Warning is normal
Choose files

## Slide 13: Waveform simulation
New「University Program VWF」file
※Remember set as Top-module before simulation

## Slide 14: WAVEFORM SIMULATION
Add test I/O
Double clicks empty space, choose「Node Finder」.
Make sure filter field are "Pins: All", click「List」and print all I/O
click「>>」select all nodes, press OK.
Double clicks

## Slide 15: Waveform simulation
•Waveform simulation interface
•Set module Input
•Start simulation
Forcing unkow
Forcing 0
Forcing 1
High impendance
clock
Functional simulation
Timing simulation
counter

## Slide 16: Waveform simulation
Use waveform simulation comfirm the results.
Changin radix for easier result observation.

## Slide 17: Simulation error
** Error (suppressible): (vsim-12110) All optimizations are disabled because the -novopt option is in effect.
Error message
This is because a feature of the simulation program has been
discontinued, but it has not been removed in this version yet.
Solution:
Simulation->Simulation Settings
Delete "–novopt" and save .

## Slide 18: Block diagram
[File]-> New -> Block Diagram / Schematic File.

## Slide 19: Block diagram
Add symbol: Double-clicks on Block Diagram empty space, choose symbol and press OK.
1.Double-Click
2.Choose component
3.click "ok" to pick up the selected component

## Slide 20: Block diagram
Generate symbol
Right click module after the compile is sucessful, choose”Create Symbol Files for Current File”.
And you can find it in the Project file.

## Slide 21: Block diagram
Wiring: Create port to every component. EX: We use the tool inside the blue box connect inst1 and inst2.

## Slide 22: Block diagram
Name: Click wire and name. The lines on the diagram dosen't need to be connected, it make the diagram more clean.

## Slide 23: Block diagram
BUS: Use a single bold line represent multiple ports, we call "Bus". The format is： Name[MSB.. LSB]，EX: wire[2..0].
The wire connected INPUT port is a multi-pin port, so the name as same as it. if we need a single port from the Bus, the naming format is: Name[bit number]. EX: wire[0], wire[1], wire[2].

## Slide 24: Block diagram
After wiring, set the ".bdf" file as top-level.
Complile, ckeck the whole circuit is correct.

## Slide 25: Layout
Pin Planner set：commonly used features are: Dip Switch、Push Button、LED、7_Segment、Clock.
Also have some output pin.
Setting circuit pin location that corresponding
the device. Like dip switch, LED...

## Slide 26: Layout
Setting the FPGA unsued pin.
Click "Device" → choose "Device and Pin Options…".
Click "Unused Pins" → make sure the option is「As input tri-stated」.
After setting pin and unused pins,
remember compile project again.
Make sure is "As input tri-stated"!!!

## Slide 27: Layout
Programming the FPGA board with VHDL code
Method 1
•Method 2

## Slide 28: LAYOUT
※:remember connect USB
Click Hardware Setup
Choose DE-SoC
1.
2.
4. Make sure device is "DE-Soc".
Need intall driver if computer dosen't detect the device.
https://blog.csdn.net/qq_43546203/article/details/116999810
3.

## Slide 29: LAYOUT
Click Auto Detect
Choose 5CSEMA5

## Slide 30: LAYOUT
Detect FPGA and HPS
Right click Device:”5CSEMA5”->
Choose Change File

## Slide 31: LAYOUT
Choose " *.sof " file.
1.
2.
Tick "Programe/Configureand" and press start

## Slide 32: FPGA introduction
Type: Cyclone V 5CSEMA5F31C6

## Slide 33
downloal USB
Power connector
Power
LED：1 for light on, 0 for light off.
Switch：1 for on 0 for down.
7-Segment Display：0 for light on, 1 for light off.
Push button : push for 0, release for 1.

## Slide 34
THE END